## Slide 1: 綠色化學的原則
Anastas & Warner (1998) 的十二條原則 (化工技術, 9(12), 128, 2001)
 盡量避免廢棄物的生成, 從源頭防治污染
 盡量使得製程中所採用的原料, 進入最終產品之中
 盡量使得所使用與產生的物質對人體健康和環境無毒無害
 盡量使得產品具有高效的功能與最低的毒性
 盡量避免使用溶劑, 分離試劑等助劑, 如不可避免時, 也要選用無毒無害的助劑

## Slide 2: 綠色化學的原則 (2)
盡量降低製程的能耗, 最好在溫和的溫度與壓力下進行
在技術可行和經濟合理的前提下, 降量採用可再生資源代替消耗性資源
盡量避免使用與產生不必要的衍生物
盡量選用高選擇性的催化劑, 這比使用化學劑量助劑更優越
改用溫和的生物製程 (酵素: 生物觸媒)
進量使產品在其成功終結後, 不會永存於環境中, 要能分解成無害的物質

## Slide 3: 綠色化學的原則 (3)
儘量在製程中即時線上監控, 有可能產生的有害物質,並儘量避免產生這些有害物質
儘量使用與產生可降低意外事故如洩漏, 爆炸,火災等的化學品

## Slide 4: 綠色化學
Green Chemistry
替代性原料
無毒性/低毒性
替代性溶劑
H2O
新觸媒
更有效率
生物程序
生物觸媒
替代性產品
提升製程效率

## Slide 5: Design Safer Chemicals
藉由分子設計概念, 使用各種合成化學 (organic/ inorganic)得到比較安全的化學品。
早期focus: efficacy of chemicals, i.e. 效用好, 成本低; 如今修正為: 必須注重對環境與與健康安全的影響與衝擊 (or 毒性)
Green Chemistry is a source prevention approach;
new chemical  structural design  safe and efficacious
existing chemicals (toxic)  structural redesign  safe and efficacious

## Slide 6: General Approaches
Reducing absorption;
Use of toxic mechanism
Use of structural-activity relationship
Use of isosteric replacement
Use of retrometabolic design
Identification of equally efficacious, less toxic chemical substitutes
Elimination of the need for associated toxic substances
ACS, 640, 1996

## Slide 7: 減少吸收 – 降低效應
毒性物質之生物化學: 知其原因, 才有對策
影響吸收的因素: physicochemical factors – molecular size, MW, dissociation constant, solubility, lipophilicity, physical state (G, L or S), particle size;
細胞膜內含有lipid, 所以lipid solubility 在腸胃內吸收角色重要;
表面積(m2) 吸收層厚度(m) 血流速(L/min)
皮膚 1.8 100-1000 0.5
小腸 200 8-12 1.4
肺部 140 0.2-0.4 5.8
Designing safer chemicals, ACS 640, 1996

## Slide 8: Toxic Mechanism
Electrophilic chemical
substances
Electrophilic metabolites
(from metabolism)
Reactions with nucleophiles
With defensive system
Reactions with nucleophiles
Of non-defensive cellular
Molecules, DNA, RNA, etc
excretion toxicity
Path I Path II

## Slide 9: Structural Modifications
1-(alkoxy)-2-propanol
R-O-CH2-C(CH2)-HOH
1-(alkoxy)-1-propanol
R-O-CH(CH2)-CH2OH
No toxicity
Toxicity
Hexane
2,5-dimethyl hexane
Neurotoxicity
No toxicity expected; BP增加40oC
藉由改變新陳代謝路徑達成降低毒性效果

## Slide 10: Use of Structure-Activity Relationship
近年來分子模擬的主要工作; sometimes called structure – property relationship;
From qualitative relationship to quantitative structure activity relationships (QSAR); 後者定量關係之建立可以靠 (i) correlation; or (ii) molecular simulation; 用於發展藥物的技巧

## Slide 11: Some Examples
Polyeoxylated nonylphenols: as surfactants/emulsifiers;
Glycidyl ethers: as reagents for synthesis;

## Slide 12: Isosteric Replacements
一個新的定義: isosteres – chemical substances, atoms, or substituents that possess near equal or similar molecular shape and volume, approximately the same distribution of electrons, and which exhibit similar physicochemical properties.
範例: 三者皆為液體, 12 & 41 沸點皆為 81oC;

## Slide 13
Metallized azo dyes:
M= Cr (toxic)
M = Fe 色澤類似, 但不具毒性

## Slide 14: Other Techniques
retrometabolic design: soft drug 觀念, i.e. 該物質很容易被新陳代謝作用轉換掉, e.g. hydrolysis step; 因而毒性降低
Equally useful, less toxic substitutes: 例如 acetoacetate 取代isocyanate in sealant and adhesive; isothiazolones for organotin as antifoulant for ships; 等
Elimination of the need for associated toxic substances: 該物質本身無毒, 但其輸送儲存時會用到毒性物質,e.g. 油漆, 水性比油性好, no or less VOC;

## Slide 15: Designing Biodegradable Chemicals
p.157-171, ACS 640, 1996;
Microbial degradation is the major loss mechanism for most organic chemicals;
一般會增加生物分解阻力者: (a) 含鹵素, esp. Cl, F; (b) 太多支鏈, branched, such as quaternary C or tertiary N; (c) nitro-, nitroso- azo- arylamino groups; (d) polycyclic residues, 尤其是超過三個以上; (e) aliphatic ether bonds, C-O-C;
生物法合成的東西大概都可以被生物分解;

## Slide 16: Biodegradable Chemicals (2)
比較喜歡: 引入oxygen in the form of hydroxyl, aldehydic, carboxylic; unsubstituted linear alkyl chains (>4) and phenyl rings;
TPBS: tetrapropylene akylbenzene sulfonate;
LAS: linear alkylbenzene sulfonate
後者比前者容易被生物分解 (一般用途: 清潔劑)

## Slide 17
前: Ethoxylated ethanaminium quaternary ammonium salt
後: ester analog of previous compound; 比較容易為生物分解